## Slide 1: Smarter Loop Exit for Level 2 Optimization

## Slide 2
Replace FixedPoint with three opportunity-producing signals
Sophia Wen — IBM Quantum
PR: qiskit#16157 Branch: pass-manager-investigation on hfwen0502/qiskit
Scope: Level 2 optimization loop only. Level 3 unchanged.

## Slide 3: Where in the transpiler?
Input circuit (abstract) │ ▼ 1. INIT — high-level optimization on abstract circuit ▼ 2. LAYOUT — virtual → physical qubit mapping ▼ 3. ROUTING — insert SWAPs to satisfy connectivity ▼ 4. TRANSLATION — convert to hardware basis gates ▼ 5. OPTIMIZATION ← we are here (a loop of passes) ▼ 6. SCHEDULING — timing / delays ▼ Output circuit (hardware-ready)
We change only stage 5, and only at optimization level 2. Stages 1–4, 6, and Level-3 stage 5 are untouched.

## Slide 4: What the Level 2 optimization stage does
After routing + translation, the circuit is hardware-legal but messy:
Routing inserted SWAPs that may now be redundant after gate cancellations.
Translation rewrote abstract gates as basis-gate sequences that may simplify.
Local 1Q runs created by both stages can often be combined into shorter sequences.
The optimization stage is a loop of passes that simplify gate by gate:
Each pass scans the DAG and rewrites local patterns.
Some passes create new opportunities for others (e.g., removing a 2Q gate exposes a longer 1Q run that the next 1Q pass can recombine).
The loop repeats until no more progress is possible — a convergence check decides when to stop.
The convergence check is what this PR changes.

## Slide 5: The Level 2 optimization pipeline (the loop body)
Each iteration runs these passes, in order:
Optimize1qGatesDecomposition CommutativeInverseCancellation (also runs in init) RemoveIdentityEquivalent ConsolidateBlocks (idle-wire contraction here, not block synthesis) CommutativeCancellation GatesInBasis ──┐ │ if False: BasisTranslator → Optimize1qGatesDecomposition ▼ Convergence check ──── re-run loop / exit
Today’s check: FixedPoint("depth", "size") — keeps re-running the loop until both metrics are unchanged for a full iteration.

## Slide 6: Pass 1 — Optimize1qGatesDecomposition
Combines runs of consecutive 1Q gates on the same qubit into a single canonical Euler decomposition, choosing the form with the fewest gates (or lowest error). Always rebuilds the run; idempotent on stable input.
Before After (target basis: sx, x, rz) q0 ──H──S──RZ(π/4)── q0 ──RZ──SX──RZ── (3 gates) (3 gates, but only physical SX once) q0 ──H──H── q0 ── (cancels to identity) (2 gates)
Key property: stateless across calls. Given the same input run, it produces the same canonical output. Re-running it without changing the runs around it cannot find new optimizations.

## Slide 7: Pass 2 — CommutativeInverseCancellation
Removes adjacent inverse pairs of gates: H·H, X·X, CX·CX, S·Sdg, etc. Runs in init as well as in the L2 loop.
Before After q0 ──H──H──●── q0 ──●── │ │ q1 ─────────⊕──CX──⊕── q1 ───⊕── (CX·CX cancelled)
Effect: removes pairs but doesn’t create new pairs. Re-running on a DAG it just simplified produces the same DAG.

## Slide 8: Pass 3 — RemoveIdentityEquivalent
Removes gates whose effect is approximately identity within an error threshold (e.g., RZ(θ) with θ ≈ 0, or 2Q rotations close to 0/2π).
Before After q0 ──RZ(1e-9)──RX(2π)── q0 ── (both ≈ I) q0 ──●── q0 ── (RZZ(2π) ≈ I, both qubits idle) │RZZ(2π) q1 ──●── q1 ──
Important for our work: when this pass removes a multi-qubit identity gate, two 1Q runs on either side merge into one — that’s a new optimization opportunity for Optimize1qGatesDecomposition.

## Slide 9: Pass 4 — ConsolidateBlocks (idle-wire contraction)
In the L2 loop, this is the idle-wire contraction form: collapses adjacent blocks of gates that act on the same qubits, removing unnecessary structure. The “block synthesis” form runs earlier.
Before After q0 ──[block A]──[block B]── q0 ──[A∘B fused]── │ │ │ q1 ────●───────────●───── q1 ────●──────────
Effect on us: rarely produces new opportunities by itself, but prepares the DAG for CommutativeCancellation to find them.

## Slide 10: Pass 5 — CommutativeCancellation
Two effects:
(a) Cancels gates across commutation boundaries. A gate on a qubit can be moved past commuting gates to find a partner to cancel with.
Before After q0 ──H──Z──H── q0 ──X── (HZH = X) q0 ──RZ(π/4)──●──RZ(-π/4)── q0 ──●── │ │ q1 ───────────⊕──────── q1 ────⊕── (RZs commute past CX, cancel)
(b) Consolidates same-axis rotations. RZ(a) · RZ(b) → RZ(a+b); same for RX. The merged angle may end up out-of-basis (triggers Signal 3, see later) or zero (then identity-removed next pass).
This pass is the biggest source of new optimization opportunities in the loop.

## Slide 11: Pass 6 — GatesInBasis → BasisTranslator
GatesInBasis is an analysis pass: it sets a property all_gates_in_basis = True / False based on whether every gate in the DAG is in the target basis.
If False, the loop runs BasisTranslator to rewrite the offending gates, then Optimize1qGatesDecomposition to clean up the (typically unoptimized) translation output.
After CommutativeCancellation merged two RZ rotations, the DAG might contain RZ(θ) where θ is a value not directly representable in the target's discrete RZ set. basis = [sx, x, rz, cz] → all in basis basis = [sx, x, rz(π/2), cz, rzz] → some RZ(θ) need translation
This is the third mechanism by which the loop finds more work to do.

## Slide 12: Today’s convergence check: FixedPoint
# Stock Qiskit, Level 2: loop = [Optimize1q, CommInvCancel, RemoveIdEquiv, Consolidate, CommCancel, GatesInBasis, ...] loop_check = FixedPoint("depth", "size") do_while_property_set("depth", "size") changes: run loop run loop_check # measures depth & size after this iteration
Behavior:
Run the full loop, measure (depth, size).
Run it again, measure again. Did either change? If yes → loop.
If both unchanged for a full iteration → exit.
The cost: even after the passes have nothing left to do, FixedPoint forces one more full iteration just to confirm. On large circuits that confirmation iteration is expensive.

## Slide 13: What we change
Instead of measuring (depth, size) after the fact, let the passes themselves report whether they created an opportunity for the next iteration.
Three orthogonal boolean signals, set by passes during their normal run:
Signal | Meaning | Set by
_opt_pass_changed | A multi-qubit gate was removed | RemoveIdentityEquivalent, CommutativeCancellation
_opt_1q_consolidated | Adjacent rotations merged | CommutativeCancellation
all_gates_in_basis == False | Out-of-basis gate produced | GatesInBasis (already present)

## Slide 14
Loop continuation rule: re-iterate iff any signal fired. If none fired, the next iteration would produce the same DAG — exit immediately.

## Slide 15: Signal 1 — multi-qubit gate removed
When RemoveIdentityEquivalent or CommutativeCancellation deletes a 2Q gate, the 1Q runs on either side merge into a longer one:
Before pass After pass q0 ──[1Q run a]──●──[1Q run b]── ──→ q0 ──[1Q run a+b]── │ removed q1 ──...──────────●──...─────── ──→ q1 ──...──────────...
The longer run gives Optimize1qGatesDecomposition new material — the canonical Euler form of (a+b) may have fewer gates than the canonical forms of a and b individually.
→ Re-run the loop.

## Slide 16: Signal 2 — rotations consolidated
When CommutativeCancellation merges adjacent same-axis rotations:
Before After q0 ──RZ(α)──[gate that commutes with RZ]──RZ(β)── ↓ q0 ──[gate]──RZ(α+β)──
The 1Q run that contained RZ(α) and RZ(β) is now shorter by one gate. Optimize1qGatesDecomposition had previously canonicalized the longer form; it can now do better on the shorter one.
→ Re-run the loop.
(Idempotent: only fires once. The next iteration’s CommutativeCancellation finds nothing new to merge.)

## Slide 17: Signal 3 — out-of-basis gate produced
CommutativeCancellation can produce a gate outside the target basis (typically a non-canonical rotation angle). GatesInBasis detects this:
basis = [sx, x, rz, cz] After CommutativeCancellation: q0 ──RZ(π/4)── all_gates_in_basis = True → done After CommutativeCancellation (different circuit): q0 ──S──Sdg──H── all_gates_in_basis = False (S, Sdg not in basis) → BasisTranslator runs, emits unoptimized sequence → Optimize1qGatesDecomposition needs another pass
→ Re-run the loop.
(This signal is the existing GatesInBasis analysis — no new code needed; it just becomes a loop-exit trigger.)

## Slide 18: Why the three signals are sufficient
Inside the L2 loop, a new optimization opportunity for the next iteration can arise only through one of these three mechanisms:
A multi-qubit gate is removed → 1Q runs on either side merge (Signal 1).
Same-axis rotations collapse → 1Q run shortens (Signal 2).
An out-of-basis gate is produced → BasisTranslator emits an unoptimized sequence (Signal 3).
Other passes in the loop (Optimize1qGatesDecomposition, CommutativeInverseCancellation, ConsolidateBlocks) are stateless on stable input: re-running them without one of the three mechanisms firing produces the same DAG.
If none of the three signals fires in an iteration, re-running the loop is provably a no-op → exit immediately.
This is what FixedPoint discovers empirically by running an extra iteration. We discover it directly.

## Slide 19: Code change footprint
6 files, +69 / −11 lines. Level 3 unchanged.
File | Change
crates/transpiler/src/passes/commutation_cancellation.rs | Returns (bool, bool) for Signals 1 + 2
crates/transpiler/src/passes/remove_identity_equiv.rs | Returns bool for Signal 1
crates/transpiler/src/passes/optimize_1q_gates_decomposition.rs | Returns bool (informational; not used as signal)
qiskit/transpiler/passes/optimization/commutative_cancellation.py | Sets _opt_pass_changed + _opt_1q_consolidated
qiskit/transpiler/passes/optimization/remove_identity_equiv.py | Sets _opt_pass_changed
qiskit/transpiler/preset_passmanagers/builtin_plugins.py | New _optimization_check_changed_flag() replaces FixedPoint at L2

## Slide 20
Signal 3 reuses the existing GatesInBasis analysis; no new code.

## Slide 21: Methodology for evidence
Suite: full benchpress/qiskit_gym/ transpile suite at optimization_level=2, 1,023 circuits across 6 groups.
Builds: Qiskit main c25216340 vs PR 5e077757e (rebased onto main), both release + mimalloc.
Seed: QISKIT_TRANSPILER_SEED=1. (=42 would resolve to 1 anyway due to a separate upstream walrus-precedence bug.)
Hardware: 2-socket Intel SPR (40c × 2 threads each socket). Main on NUMA 0, PR on NUMA 1, parallel. NUMA sweep validated single- socket pinning is within 1.7% of full-machine on hwb12.
Benchpress patch: 2-line diff adds total/1Q gate count + total/1Q depth alongside existing 2Q metrics; FlexibleBackend gets fixed seed=12345 so abstract tests see deterministic backend targets.
Bug-2 exclusion: 2 circuits (1 in device_hamiltonians, 1 in abstract_hamiltonians) hit a pre-existing upstream non-determinism (1Q rotation tie-break). 2Q counts identical on both, only 1Q drift. Excluded from aggregate; reproducer included.

## Slide 22: Per-group results (1,021 circuits, all bit-identical)
Group | Circuits | 2Q count Δ | Total count Δ | Total depth Δ | Wall-clock
feynman | 50 | 0 | 0 | 0 | −22.7%
device_hamiltonians | 80 | 0 | 0 | 0 | −17.5%
abstract_small | 168 | 0 | 0 | 0 | −9.5%
abstract_medium | 92 | 0 | 0 | 0 | −19.1%
abstract_large | 232 | 0 | 0 | 0 | −17.5%
abstract_hamiltonians | 399 | 0 | 0 | 0 | −10.3%
Total | 1,021 | 0 | 0 | 0 | −16.2%

## Slide 23
Zero delta on every gate / depth metric across every group. Aggregate −16.2% wall-clock, range −9.5% to −22.7%, no slowdowns >5%.

## Slide 24: Headline speedups (per-circuit, end-to-end pm.run())
Circuit | Group | Main | PR | Speedup
hwb12 | feynman | 14.40 s | 10.85 s | −24.7%
hwb11 | feynman | 6.76 s | 5.19 s | −23.2%
100-linear | abstract_large | 6.39 s | 4.68 s | −26.7%
vqe_uccsd_n28-square | abstract_large | 18.09 s | 13.62 s | −24.7%
bwt_n37-linear | abstract_large | 67.38 s | 50.81 s | −24.6%
multiplier_n400-linear | abstract_large | 26.24 s | 19.91 s | −24.1%
factor247_n15-heavy-hex | abstract_medium | 14.33 s | 11.03 s | −23.0%
ham_gnp-k_5_n-90_rinst-02 | abstract_hams (linear) | 0.75 s | 0.55 s | −26.4%

## Slide 25
Wall-clock is end-to-end transpile (pipeline-wide); loop-only speedup is larger but not directly measured by these runs.

## Slide 26: Stress test: hwb12
hwb12.qasm (Hidden Weighted Bit, 12 qubits, ~190K input gates) is Matthew’s go-to stress test for the L2 loop because the loop processes >1M gates after pre-loop block consolidation.
 | Main | PR | Δ
End-to-end transpile | 14.40 s | 10.85 s | −24.7%
2Q gate count | 644,633 | 644,633 | 0
1Q gate count | 1,752,972 | 1,752,972 | 0
Total depth | 1,074,718 | 1,074,718 | 0

## Slide 27
Bit-identical output on every metric, end-to-end −24.7%.
Earlier loop-only measurement: +47% / −32% wall-clock (4.0s vs 5.8s loop-body), confirming the wall-clock win is the loop, not noise.

## Slide 28: Two upstream Qiskit issues found (not caused by this PR)
Bug 1 — walrus precedence in QISKIT_TRANSPILER_SEED parsing
# Current (buggy) — `:=` binds looser than `is not None` if seed := os.getenv("QISKIT_TRANSPILER_SEED", None) is not None: seed_transpiler = int(seed) # Result: seed_transpiler is always 0 or 1 regardless of env-var value. # Fix: if (seed := os.getenv("QISKIT_TRANSPILER_SEED", None)) is not None: seed_transpiler = int(seed)
Pure-Python reproducer in evidence tarball. Will be filed upstream separately.
Bug 2 — unseeded RNG in 1Q rotation tie-break
2 of 1,023 circuits give different 1Q decompositions across fresh Python subprocesses, even with seed_transpiler pinned. 2Q count unchanged on both. Reproducer in tarball.
Both bugs predate this PR. Excluded from analysis to avoid distorting results.

## Slide 29: Status
PR #16157: open, ready for re-review.
Gate | Status
PR template + AI/LLM disclosure | ✅
CLA signed | ✅
Commit authorship | ✅
Rebased on current main, no merge conflicts | ✅
Evidence — full benchpress + raw JSONs + scripts attached as tarball | ✅
Per-group + total no-regression on 6 metrics | ✅
Wall-clock speedup data | ✅
Re-review requested | ✅

## Slide 30
Next: respond to any further review comments; file Bugs 1 and 2 as separate issues; prep follow-up PRs if Matthew wants the same shape at Level 3.